## Slide 1: Ebola Virus Disease (EVD) Laboratory Diagnostics
04/12/2014

## Slide 2: Ebola Virus Disease Laboratory Criteria Case Defintion
Any of the following:
Detection of Ebola virus nucleic acid in a clinical specimen and confirmation by sequencing or a second assay on different genomic targets.
    Testing is performed by the National Virus Reference Laboratory (NVRL), which is based on campus in University College Dublin (UCD)
    A Biosafety Level 3 Facility
Isolation of Ebola virus from a clinical specimen
    Requires Biosafety Level 4 Facility not available in Ireland

## Slide 3: Diagnostic Assays [1]
Ebola is a single stranded RNA virus
Genome is 18- 19 kb in size
The genome encodes for 7 viral proteins

## Slide 4: Diagnostic Assays [2]
1
2
The NVRL performs two tests on each sample. Each assay has a different target.
Commercial real time Polymerase Chain Reaction (PCR) assay targeting the L (polymerase) gene
In-house PCR assay targeting the GP (glycoprotein) gene
The tests are run at the same time.

## Slide 5: Requesting a test for EVD [1]
Decision to request EVD test
  Refer to the Ebola Virus Disease Risk Assessment Algorithm available at www.hpsc.ie
Sample collection
  EDTA and serum (whole clotted blood sample) required
  Sample volume of 5ml
    In certain cases e.g. paediatric patients smaller volumes may be acceptable (contact the NVRL to discuss)
  Sample should be received by NVRL within 12 hours of collection but ideally as soon as possible.

## Slide 6: Requesting a test for EVD [2]
Contact the NVRL
  Telephone the NVRL PRIOR to sending the sample
    Tel: 01 7164401 or out of hours mobile: 087 9806448
  Testing is available for high-risk exposure cases twenty four hours a day, seven days a week
Ensure specimens are labeled correctly and a test request form is completed
  Available at http://nvrl.ucd.ie/

## Slide 7: Packaging & Transport [1]
Ebola is classified as a Category A Infectious Substances (UN2814) and should be packaged in accordance with international regulations
Transport to the NVRL via the designated national courier service for EVD samples
©www.cdc.gov

## Slide 8: Testing Process [1]
Main corridor
BL3 laboratory
-50Pa
Class
I/ III
MSC
Class
III
MSC
Shower
-10Pa
Outer lobby
Inner lobby
-35Pa
-20oC
-80oC
CO2
Inc.
40C
+10Pa
18 ac/h
Pass through
autoclave
Containment envelope
On receipt in the NVRL the sample is taken directly to the Biosafety Level 3 Laboratory.

## Slide 9
The specimen is unpacked, prepared & undergoes centrifugation.
RNA Extraction is performed. The addition of Guanidine thiocyanate inactivates the virus and PCR analysis can be performed in the Biosafety Level 2 Laboratory.
PCR analysis is performed.
Two assays with two separate targets which are run in parallel.
B
S
L
3
B
S
L
2

## Slide 10: Testing Process [3]
  The turn around time for testing in most cases is approx. 6 hours from receipt of sample in the NVRL
Results will be communicated directly to the requesting clinician as soon as they are available. Please do not contact the NVRL for the result
A negative RT-PCR test result for Ebola virus from a blood specimen collected less than 72 hours after onset of symptoms does not necessarily rule out Ebola virus infection
The need to repeat the EVD test and the timing of sample collection for the repeat test will be discussed on a case by case basis

## Slide 11: Key Messages
Refer to the Ebola Virus Disease Risk Assessment Algorithm available at www.hpsc.ie , for details on how to request an EVD test
    Contact the NVRL prior to sending a sample
      Tel: 01 7164401 or out of hours mobile 087 9806448
Results will be communicated to the designated person as soon as they are available (approx. 6 hours)

## Slide 12: National Virus Reference Laboratory Contact Information
For up to date information on EVD laboratory testing please see the NVRL Website: http://nvrl.ucd.ie
For clinical enquiries contact (01) 7164401